DIGITAL DESIGN SAP VERILOG ASSIGNMENT REPORT
IMT2016129
Ananth Shreekumar

The above image shows the signals of SAP as a function of time. The reset is asynchronous. All signals

The below image shows the values held by all the registers – Program counter, MAR, RAM, Instruction register, Controller, Accumulator, Adder/Subractor, B register and Output register (IN THAT ORDER) as a function of time. All the values are in HEXADECIMAL.
Hence the final value 82 in hex is 130 in decimal.

The below image shows the value of the Wire Bus as a fucntion of time.All values are in hexadecimal.

Output=0 occurs at the beginning just to indicate that the SAP is starting from scratch.
Output=129 occurs after loading 129 (my roll number). Then, ADD 16 and SUB 15 gives 130 which is displayed by Output=130.

The below image shows the ring counter generated in Controller/Sequencer.
The last cycle does NOT have the 3 execute cycles because it is OUT instruction.

Source Code:

Program Counter

module ProgramCounter (
    clk, // <i
    clr, // <i
    Ep, // <i
    Cp, // <i
    busOut // >o
);

input clk, clr, Ep, Cp;
output [3:0] busOut;

reg [3:0] CurrentCounterValue;

initial begin
    CurrentCounterValue = 4'd0;
end

always @(posedge clk) begin
    if (clr) begin // reset
        CurrentCounterValue = 4'd0;
    end
    else begin
        if (Cp) begin
        CurrentCounterValue = CurrentCounterValue + 4'd1;
        end
        else begin
        CurrentCounterValue = CurrentCounterValue;
        end
    end
end

// output
assign busOut = (Ep)? CurrentCounterValue : 4'bz;
endmodule

Memory Address Register

module MemoryAddressRegister (
    clk, // <i
    Lm, // <i
    busIn, // <i
    Address // >o
);

input clk, Lm;
input [3:0] busIn;
output [3:0] Address;

reg [3:0] Address;

initial begin
    Address = 4'd0;
end

always @(posedge clk) begin
    if (Lm) begin
        Address = busIn;
    end
    else begin
        Address = Address;
    end
end

endmodule

RAM

module Ram (
    Address, // <i
    Ce, // <i
    busOut // >0
);

input [3:0] Address;
input Ce;
output [7:0] busOut;

wire [7:0] Mem [0:15];

wire [7:0] Data;

assign busOut = (Ce)? Data : 8'bz;

assign Data = Mem[Address];

endmodule
Instruction Register

module InstructionRegister (
    clk, // <i
    clr, // <i
    Ei, // <i
    Li, // <i
    busIn, // <i
    busOut, // >o
    opCode // >o
);

input clk, clr, Ei, Li;
input [7:0] busIn;
output [3:0] busOut;
output [3:0] opCode;

reg [7:0] CurrentInstructionValue;

initial begin
    CurrentInstructionValue = 8'd0;
end

always @(posedge clk) begin
    if (clr) begin // reset
        CurrentInstructionValue = 8'hFF; // halt instruction by default
    end
    else begin
        if (Li) begin
        CurrentInstructionValue = busIn;
        end
        else begin
        CurrentInstructionValue = CurrentInstructionValue;
        end
    end
end

// output
assign busOut = (Ei)? CurrentInstructionValue : 4'bz;
assign opCode = CurrentInstructionValue[7:4];
endmodule

Controller

module Controller (
    opCode, // <i
    reset, // <i
    Ce, // >o
    Cp, // >o
    Ea, // >o
    Ei, // >o
    Ep, // >o
    Eu, // >o
    La, // >o
    Lb, // >o
    Li, // >o
    Lm, // >o
    Lo, // >o
    Su, // >o
    clk, // >o
    clr // >o
// we // >o
);

input [3:0] opCode;
input reset;
output Ce;
output Cp;
output Ea;
output Ei;
output Ep;
output Eu;
output La;
output Lb;
output Li;
output Lm;
output Lo;
output Su;
output clk;
output clr;
//output we;

reg Ce;
reg Cp;
reg Ea;
reg Ei;
reg Ep;
reg Eu;
reg La;
reg Lb;
reg Li;
reg Lm;
reg Lo;
reg Su;
reg clr;
// reg we;

ClockGen clkgen0 (
    .clk(clk)
);

reg [5:0] T;

initial begin
    T = 6'd1;
end

always @(negedge clk) begin
    clr = 0;
    if (reset) begin
        T = 6'd1;
        clr = 1;
    end
    else if (T[2] && opCode == 4'hF) begin
        T = 6'd0;
    end
    else if (T[5]) begin
        T = 6'd1;
    end
    else begin
        T = T << 1;
    end
end

wire T1 = T[0];
wire T2 = T[1];
wire T3 = T[2];
wire T4 = T[3];
wire T5 = T[4];
wire T6 = T[5];

// T1 state
always @(T1) begin
    Ep = 0;
    Lm = 0;
    if (T1) begin
        Ep = 1;
        Lm = 1;
    end
end

// T2 state
always @(T2) begin
    Cp = 0;
    if (T2) begin
        Cp = 1;
    end
end

// T3 state
always @(T3) begin
    Ce = 0;
    Li = 0;
    if (T3) begin
        Ce = 1;
        Li = 1;
    end
end

// T4 state
always @(T4 or T5 or T6) begin
    Ei = 0;
    Lm = 0;
    Ce = 0;
    La = 0;
    Lb = 0;
    Su = 0;
    Eu = 0;
    Lo = 0;
    Ea = 0;
// we = 0;

    case (opCode)
        4'h0:
        if (T4) begin
        Ei = 1;
        Lm = 1;
        end
        else if (T5) begin
        Ce = 1;
        La = 1;
        end
        4'h1:
        if (T4) begin
        Ei = 1;
        Lm = 1;
        Su = 0;
        end
        else if (T5) begin
        Ce = 1;
        Lb = 1;
        Su = 0;
        end
        else if (T6) begin
        Eu = 1;
        La = 1;
        Su = 0;
        end
        4'h2:
        if (T4) begin
        Ei = 1;
        Lm = 1;
        Su = 1;
        end
        else if (T5) begin
        Ce = 1;
        Lb = 1;
        Su = 1;
        end
        else if (T6) begin
        Eu = 1;
        La = 1;
        Su = 1;
        end
        /*
        4'h3:
        if (T4) begin
        Ei = 1;
        Lm = 1;
        end
        else if (T5) begin
        Ea = 1;
        we = 1;
        end
        */
        4'hE:
        if (T4) begin
        Ea = 1;
        Lo = 1;
        end
    endcase
end

endmodule

Accumulator

module Accumulator (
    clk, // <i
    Ea, // <i
    La, // <i
    busIn, // <i
    Avalue, // >o
    busOut // >o
);

input clk, Ea, La;
input [7:0] busIn;
output [7:0] busOut;
output [7:0] Avalue;

reg [7:0] accumulator;

initial begin
    accumulator = 8'd0;
end

always @(posedge clk) begin
    if (La) begin
        accumulator = busIn;
    end
    else begin
        accumulator = accumulator;
    end
end

// output
assign busOut = (Ea)? accumulator : 8'bz;
assign Avalue = accumulator;
endmodule

Adder/Subtracter(ALU)

module AdderSubractor (
    Eu, // <i
    Su, // <i
    Ain, // <i
    Bin, // <i
    Output // >o
);

input Eu, Su;
input [7:0] Ain;
input [7:0] Bin;
output [7:0] Output;

wire [8:0] Result;

// Arithmetic logic
assign Result = (Su)? Ain - Bin : Ain + Bin;

// output
assign Output = (Eu)? Result[7:0] : 8'bz;
endmodule

B Register

module Bregister (
    clk, // <i
    Lb, // <i
    busIn, // <i
    Bvalue // >o
);

input clk, Lb;
input [7:0] busIn;
output [7:0] Bvalue;

reg [7:0] Bvalue;

initial begin
    Bvalue = 8'd0;
end

always @(posedge clk) begin
    if (Lb) begin
        Bvalue = busIn;
    end
    else begin
        Bvalue = Bvalue;
    end
end
endmodule
Output Register

module OutputRegister (
    clk, // <i
    Lo, // <i
    busIn, // <i
    Ovalue // >o
);

input clk, Lo;
input [7:0] busIn;
output [7:0] Ovalue;

reg [7:0] Ovalue;

initial begin
    Ovalue = 8'd0;
end

always @(posedge clk) begin
    if (Lo) begin
        Ovalue = busIn;
    end
    else begin
        Ovalue = Ovalue;
    end
end
endmodule

Binary Display

module BinaryDisplay (
    Ovalue // <i
);

input[7:0] Ovalue;

always @(*) begin
    $display ("Output = %d", Ovalue);
end

endmodule

SAP This module binds together all other individual modules

`include "Accumulator.v"
`include "AdderSubtractor.v"
`include "BinaryDisplay.v"
`include "Bregister.v"
`include "ClockGen.v"
`include "Controller.v"
`include "InstructionRegister.v"
`include "MemoryAddressRegister.v"
`include "OutputRegister.v"
`include "ProgramCounter.v"
`include "Ram.v"

module SAP (
    reset // <i
);

input reset;

wire [7:0] Wbus;
wire Ce, Cp, Ea, Ei, Ep, Eu, La, Lb, Li, Lm, Lo, Su, clk, clr;
wire [3:0] Address;
wire [3:0] opCode;
wire [7:0] Avalue;
wire [7:0] Bvalue;
wire [7:0] Ovalue;

// wire We; TODO use this to enhance the "SAP"

Accumulator A0(
    .clk(clk), // <i
    .Ea(Ea), // <i
    .La(La), // <i
    .busIn(Wbus), // <i
    .Avalue(Avalue), // >o
    .busOut(Wbus) // >o
);

AdderSubractor ALU0(
    .Eu(Eu), // <i
    .Su(Su), // <i
    .Ain(Avalue), // <i
    .Bin(Bvalue), // <i
    .Output(Wbus) // >o
);

BinaryDisplay DISP0(
    .Ovalue(Ovalue) // <i
);

Bregister B0(
    .clk(clk), // <i
    .Lb(Lb), // <i
    .busIn(Wbus), // <i
    .Bvalue(Bvalue) // >o
);

InstructionRegister IR0(
    .clk(clk), // <i
    .clr(clr), // <i
    .Ei(Ei), // <i
    .Li(Li), // <i
    .busIn(Wbus), // <i
    .busOut(Wbus[3:0]), // >o
    .opCode(opCode) // >o
);

MemoryAddressRegister MAR0(
    .clk(clk), // <i
    .Lm(Lm), // <i
    .busIn(Wbus[3:0]), // <i
    .Address(Address) // >o
);

OutputRegister O_R0(
    .clk(clk), // <i
    .Lo(Lo), // <i
    .busIn(Wbus), // <i
    .Ovalue(Ovalue) // >o
);

ProgramCounter PC0(
    .clk(clk), // <i
    .clr(clr), // <i
    .Ep(Ep), // <i
    .Cp(Cp), // <i
    .busOut(Wbus[3:0]) // >o
);

Ram RAM0(
    //.clk(clk), // <i TODO use this to enhance the "SAP"
    //.We(We), // <i TODO use this to enhance the "SAP"
    //.busIn(Wbus), // <i TODO use this to enhance the "SAP"
    .Address(Address), // <i
    .Ce(Ce), // <i
    .busOut(Wbus) // >0
);

Controller CONTROL0(
    .opCode(opCode), // <i
    .reset(reset), // <i
    .Ce(Ce), // >o
    .Cp(Cp), // >o
    .Ea(Ea), // >o
    .Ei(Ei), // >o
    .Ep(Ep), // >o
    .Eu(Eu), // >o
    .La(La), // >o
    .Lb(Lb), // >o
    .Li(Li), // >o
    .Lm(Lm), // >o
    .Lo(Lo), // >o
    .Su(Su), // >o
    .clk(clk), // >o
    .clr(clr) // >o
// .we(we) // >o
);

endmodule

Clock Generator

module ClockGen (
    clk // >o
);

output clk;

reg clk;

initial begin
    clk = 0;
    forever begin
        #50 clk = !clk;
    end
end

endmodule

Test Bench

`include "SAP.v"

module tb();

reg reset;

SAP SAP0 (
    .reset(reset)
);

initial begin
    reset = 1;

    // RAM data initializations
    // PROGRAM MEMORY
    force SAP0.RAM0.Mem[0] = {4'h0, 4'h9};
    force SAP0.RAM0.Mem[1] = {4'hE, 4'hA};
    force SAP0.RAM0.Mem[2] = {4'h1, 4'hA};
    force SAP0.RAM0.Mem[3] = {4'h2, 4'hB};
    force SAP0.RAM0.Mem[4] = {4'hE, 4'hA};
    force SAP0.RAM0.Mem[5] = {4'hF, 4'hA};
    force SAP0.RAM0.Mem[6] = {4'hA, 4'hA};
    force SAP0.RAM0.Mem[7] = {4'hA, 4'hA};
    force SAP0.RAM0.Mem[8] = {4'hA, 4'hA};

    // DATA MEMORY
    force SAP0.RAM0.Mem[9] = {8'd129};
    force SAP0.RAM0.Mem[10] = {8'd16};
    force SAP0.RAM0.Mem[11] = {8'd15};
    force SAP0.RAM0.Mem[12] = {8'hAA};
    force SAP0.RAM0.Mem[13] = {8'hAA};
    force SAP0.RAM0.Mem[14] = {8'hAA};
    force SAP0.RAM0.Mem[15] = {8'hAA};

    #225

    reset = 0;

    #5000
    $finish;

end

initial
begin
    $dumpfile("SAP.vcd");
    $dumpvars(0,SAP0);
end

endmodule
To run the program, create files for each module and type the command

        iverilog tb.v

in the terminal to create an instance a.out.

The command

        a.out

gives the output.